## Slide 1
MY AITU / ICT ASSIGNMENT 4
01 / 19
ASSIGNMENT 04
Multimedia
Technologies
The media layer of My AITU
Formats, optimisation and accessible design
for the LMS bridge prototype.
Salima Zimbekkyzy · Azhar Saparzholova
Nurassyl Oralbekov
SE-2623 / ICT
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 1 Multimedia Technologies Assignment 4 Team: Salima Zimbekkyzy, Azhar Saparzholova, Nurassyl Oralbekov Group: SE-2623 Course: ICT Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 2
PART A / FORMAT STRATEGY
Choose the format for the job
Three questions guide every choice: what is it, where is it used, and what must stay sharp?
MY AITU / ICT ASSIGNMENT 4
02 / 19
MEDIA | DECISION TO MAKE | PROJECT APPLICATION
Images | Balance crisp interface details against file size. | WebP preview, PNG source and SVG icons
Audio | Separate distribution files from editing masters. | If narration is added: AAC / MP3; WAV for editing
Video | Choose both a container and a codec. | Planned: MP4 with H.264 video and AAC audio
01
QUALITY
02
FILE SIZE
03
COMPATIBILITY
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 2 Part A — Multimedia formats | | | | | | | | Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 3
A1 / FORMAT COMPARISON
One table. Ten media formats.
MY AITU / ICT ASSIGNMENT 4
03 / 19
FORMAT | TYPE | COMPRESSION | ALPHA / MOTION | TYPICAL SIZE | SUPPORT | PROJECT USE
PNG | Image | Lossless | Alpha; APNG | Large photos | Broad | UI evidence
JPEG | Image | Lossy | None | Small photos | Broad | Photos
WebP | Image | Both modes | Alpha; motion | Compact | Modern | App preview
SVG | Image | Vector / text | Alpha; motion | Tiny icons | Broad | UI icons
MP3 | Audio | Lossy | N/A | Small | Broad | Speech / music
AAC / M4A | Audio | Lossy | N/A | Small | Broad* | Narration
WAV / PCM | Audio | Uncompressed | N/A | Large | Broad* | Editing master
MP4 / H.264 | Video | Usually lossy | Motion | Bitrate-based | Broad* | Demo delivery
WebM / VP9 | Video | Usually lossy | Motion; alpha* | Bitrate-based | Modern* | Web playback
MOV / H.264 | Video | Usually lossy | Motion | Bitrate-based | Limited web | Editing / transfer
Container = the package. Codec = how the media is encoded.
*Support depends on codec, OS and device. Size varies with content, resolution, bitrate and duration.
Sources cited in the original: MDN Image file type guide; Media container formats.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 3 A1. Format comparison Format Type Compression Alpha / motion Typical size Support Project use PNG Image Lossless Alpha; APNG Large photos Broad UI evidence JPEG Image Lossy Neither Small photos Broad Photos WebP Image Both modes Alpha + motion Compact Modern App preview SVG Image Vector / text Alpha + motion Tiny icons Broad UI icons MP3 Audio Lossy N/A Small Broad Speech / music AAC (M4A) Audio Lossy N/A Small Broad* Narration WAV (PCM) Audio Uncompressed N/A Large Broad* Editing master MP4 H.264 Video Usually lossy Motion; no alpha Bitrate-based Broad* Demo delivery WebM VP9 Video Usually lossy Motion; alpha* Bitrate-based Modern* Web playback MOV H.264 Video Usually lossy Motion; no alpha Bitrate-based Limited web Editing / transfer A container (MP4) packages tracks and metadata; a codec (H.264) encodes and decodes the media. *Codec, OS and device support vary. File size depends on content, resolution, bitrate and duration. Sources: MDN, Image file type guide and Media container formats. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 4
A2 / MEASURED EXPERIMENT
Same screen. Four encodings.
390 × 844 pixels in every file. Measurements use binary KiB: 1 KiB = 1024 bytes.
MY AITU / ICT ASSIGNMENT 4
04 / 19
FORMAT / SETTING | SIZE (KiB) | VISUAL OBSERVATION
PNG | 58.39 | Sharp source
JPEG Q80 | 28.72 | Minor edge artifacts
JPEG Q40 | 16.49 | Visible edge artifacts
WebP Q80 | 15.75 | Readable, compact
73.0%
smaller than PNG
WebP Q80 saves 42.64 KiB
at the original resolution.
VIDEO EVIDENCE PENDING
The same 10-second clip still needs two measured exports.
PNG / WebP: supplied files. JPEGs: exported from the same PNG at Q80 / Q40, 4:2:0 chroma, optimised, 25 Oct 2026.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 4 A2. Measured experiment Project file / export Setting and dimensions Size (KiB) Quality evidence attendance-preview.png PNG, 390 × 844 px 58.39 Original; visual check pending attendance-preview.jpg JPEG Q80, 390 × 844 px Not supplied Export + inspect attendance-preview-low.jpg JPEG Q40, 390 × 844 px Not supplied Export + inspect attendance-preview.webp WebP Q80, 390 × 844 px 15.75 In app; visual check pending 10-second clip, version 1 Proposed: MP4 H.264, 720p Not supplied Record + export 10-second clip, version 2 Same clip, lower video bitrate Not supplied Compare text and motion 42.64 KiB saved per preview 58.39 → 15.75 KiB: 73.0% smaller at the same resolution. Source: supplied project inventory, 23 Oct 2026. 1 KiB = 1024 bytes. JPEG and clip rows are a test plan, not completed measurements. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 5
A2 / VISUAL EVIDENCE
Look at the edges, not just the number.
Identical 360 × 360 pixel crops, displayed at the same scale.
MY AITU / ICT ASSIGNMENT 4
05 / 19
PNG
58.39 KiB
Crisp source text
JPEG Q80
28.72 KiB
Light halos on edges
JPEG Q40
16.49 KiB
More obvious ringing
WebP Q80
15.75 KiB
Readable UI details
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 5 A2. Visual quality check What the quality comparison must show Use the same attendance screen in all four exports. Compare an identical crop at 100% zoom so text edges and calendar lines remain comparable. PNG Actual project crop required here JPEG Q80 Actual project crop required here JPEG Q40 Actual project crop required here WebP Q80 Actual project crop required here Evidence still needed One side-by-side screenshot, JPEG file sizes, and two exports of the same 10-second clip. Rate each result as sharp, acceptable or poor after inspection. The source image and recording were not included in the supplied files. These boxes mark missing evidence. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 6
A2 / OUR FORMAT CHOICES
Smaller files. Same screen dimensions.
MY AITU / ICT ASSIGNMENT 4
06 / 19
Preview image size (KiB)
Chart: 
| PNG | WebP Q80
KiB | 58.39 | 15.75
42.64 KiB saved per preview
1
WebP Q80
Use for the attendance preview.
2
PNG
Retain the lossless evidence image.
3
Inline SVG + CSS
Use vectors for icons and CSS for motion.
File-size reduction does not prove faster network loading.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 6 A2. Our format choices 73% smaller preview file For the My AITU / LMS bridge, we use WebP at quality 80 for the attendance preview. At the same 390 × 844 resolution, its file size falls from 58.39 KiB to 15.75 KiB, saving 42.64 KiB, or 73.0%. We retain PNG as the original evidence image because it preserves text and edges without lossy compression. Inline SVG suits interface icons because vectors stay sharp at different sizes and share the HTML response. CSS provides the login pulse without a separate video download. For the project demonstration, we plan MP4 with H.264 video and AAC audio for broad playback support. JPEG settings and the ten-second clip still need measured comparison before we can report their quality or size. Same pixels. Less data. PNG 58.39 KiB WebP 15.75 KiB Measured file sizes only. Network speed needs its own test. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 7
B1 / INTERFACE ICONS
18 icons. One HTML response.
Inline SVG markup is embedded in the page; the values below are source bytes, not separate downloads.
MY AITU / ICT ASSIGNMENT 4
07 / 19
ASSET | WHERE USED | BYTES
3 · Book | Courses / nav | 740
4 · Calendar | Tasks / attendance | 1,162
5 · Graduation | Grades | 857
6 · User | Account | 869
7 · Menu | Navigation | 561
8 · Close | Navigation | 441
9 · Down | Account menu | 391
10 · Sign-out | Account menu | 906
11 · Refresh | Reload | 945
ASSET | WHERE USED | BYTES
12 · Search | Course search | 669
13 · Eye | Password visibility | 935
14 · Check | Attendance | 366
15 · Absent | Attendance | 442
16 · Clock | Attendance time | 777
17 · Minus | Unmarked status | 284
18 · Left arrow | Previous month | 416
19 · Next arrow | Next month | 404
20 · List | Attendance status | 1,010
Flaticon Uicons Regular Rounded · SVG viewBox 300 × 300 · Free licence with visible footer attribution.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 7 B1. Interface icons # Asset Where used Vector viewBox Markup size 3 Book Courses / navigation SVG 300 × 300 740 B 4 Calendar Tasks / attendance SVG 300 × 300 1,162 B 5 Graduation Grades SVG 300 × 300 857 B 6 User Account button SVG 300 × 300 869 B 7 Menu Navigation button SVG 300 × 300 561 B 8 Close Navigation controls SVG 300 × 300 441 B 9 Down Account menu SVG 300 × 300 391 B 10 Sign-out Account menu SVG 300 × 300 906 B 11 Refresh Reload SVG 300 × 300 945 B 12 Search Course search SVG 300 × 300 669 B 13 Eye Password visibility SVG 300 × 300 935 B 14 Check Attendance SVG 300 × 300 366 B All icons: Flaticon Uicons Regular Rounded. Free licence with visible footer attribution. Inline symbols share the HTML response; these are source sizes, not separate requests. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 8
B1 / ASSET INVENTORY
The rest of the media stack
25 assets in the inventory: 18 icons and these seven visual, type and support elements.
MY AITU / ICT ASSIGNMENT 4
08 / 19
ASSET | WHERE | FORMAT / DIMENSIONS | SIZE | SOURCE / LICENCE
1 · Attendance preview | Sign-in | WebP · 390 × 844 | 15.75 KiB | Own + icons¹
2 · LMS wordmark | Sign-in | CSS / text · 68 × 68 | Embedded | Own
21 · Login pulse | Login progress | CSS · 2 s loop | Embedded | Own
22 · Entrance motion | Transitions | CSS · 0.4 s | Embedded | Own
23 · Campus map | Map section | Responsive iframe | Variable | Yuujiso · MIT²
24 · Inter font | Interface | Web font · variable | Variable | Inter · OFL³
25 · Remote view | Optional support | JPEG Q70 · 1100 × 800 | Variable | Private session
¹ Flaticon attribution in footer. ² github.com/Yuujiso/aitumap. ³ github.com/rsms/inter.
The remote browser view is private and must stay out of the demo. Evidence PNGs and two unused SVG symbols are not loaded by the interface.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 8 B1. Media asset inventory # Asset Where used Format / dimensions Size Source / licence 15 Absent icon Attendance SVG 300 × 300 442 B Flaticon¹ 16 Clock icon Attendance time SVG 300 × 300 777 B Flaticon¹ 17 Minus icon Unmarked attendance SVG 300 × 300 284 B Flaticon¹ 18 Left arrow icon Previous month SVG 300 × 300 416 B Flaticon¹ 19 Next arrow icon Next month SVG 300 × 300 404 B Flaticon¹ 20 List icon Attendance status SVG 300 × 300 1,010 B Flaticon¹ 1 Attendance preview Sign-in WebP 390 × 844 15.75 KiB Own + icons¹ 2 LMS wordmark Sign-in CSS / text, 68 × 68 Embedded Own 21 Login pulse Login progress CSS, 2 s loop Embedded Own 22 Entrance motion Transitions CSS, 0.4 s Embedded Own 23 Campus map Map section Responsive iframe Variable Yuujiso / MIT² 24 Inter font Interface text Web font / weights Variable Inter / OFL³ 25 Remote view Optional support JPEG Q70, 1100 × 800 Variable Private session ¹ Flaticon attribution in footer. ² github.com/Yuujiso/aitumap (MIT), author beside map. ³ github.com/rsms/inter (SIL OFL 1.1). Remote session views must stay out of the submitted demo. Unused ui-right / ui-stats and evidence PNG files are not loaded by the running interface. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 9
B2 / INTEGRATION & OPTIMISATION
A lighter payload, with clear limits.
MY AITU / ICT ASSIGNMENT 4
09 / 19
73.0%
smaller preview
30.8%
smaller controlled file set
0
expected image-request delta
CONTROLLED LOCAL PAYLOAD | PNG VERSION | WEBP VERSION | CHANGE
Preview image | 59,787 B | 16,126 B | −73.0%
4 front-end files + preview | 141,601 B | 97,941 B | −30.8%
Integrated
Responsive 250 px preview, inline SVG icons, CSS login pulse and reduced-motion support.
Still to measure
DevTools: transferred bytes, requests and Finish/Load time on Fast 4G with cache disabled.
Source: Part B inventory, 23 Oct 2026. Calculated local file bytes; external traffic and compression are excluded.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 9 B2. Integration and optimisation What is integrated WebP preview: 390 × 844 px, displayed at 250 px wide. 18 inline SVG icons and a CSS login pulse. Reduced-motion preference disables animation. The full page still needs a 360 px browser check. Controlled local payload Before: PNG After: WebP Change Preview image 59,787 B 16,126 B −73.0% 4 front-end files + preview 141,601 B 97,941 B −30.8% DevTools measurements: still required Disable cache, select Fast 4G, reload the same screen before and after. Capture transferred bytes, request count and Finish/Load time. Image-request delta should be 0; verify the total. The payload calculation excludes headers, compression, API, fonts and map traffic. Stage 1 requires <3 s per request at 1,000 users; this remains unverified. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.The 30.8% is a controlled local file-payload calculation, not a browser Network measurement. Headers, compression, API calls, Google Fonts and iframe traffic are excluded. The 360 px viewport check and <3 s at 1,000 users remain unverified. See assignment4/part_b.md.

## Slide 10
B3 / MEDIA ACCESSIBILITY
Make the experience understandable.
Implemented behaviours and checks from the prototype inventory.
MY AITU / ICT ASSIGNMENT 4
10 / 19
IMPLEMENTED
Descriptive alt text
The attendance preview describes the calendar and status counts.
IMPLEMENTED
Decorative SVGs
Icons are hidden from screen readers; controls keep text or labels.
IMPLEMENTED
Reduced motion
The user’s preference disables animations and transitions.
IMPLEMENTED
Visible progress
Login progress has text and a visual pulse. No sound-only information.
NOT APPLICABLE
Captions / transcript
No speech audio or video is embedded in the prototype.
NOT APPLICABLE
Text over images
Captions sit below images; live text does not overlay raster images.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 10 B3. Accessibility of media Meaningful images have descriptive alt text The test attendance preview describes the month and status counts. Decorative SVGs use aria-hidden="true"; controls retain text or accessible labels. <img src="/attendance-preview.webp" width="390" height="844" alt="Тестовый экран посещаемости: календарь за октябрь 2026 года и счётчики — 0 присутствий, 1 пропуск, 0 опозданий, 1 запись без отметки."> Motion follows the user’s preference @media (prefers-reduced-motion: reduce) { *, *::before, *::after { animation: none !important; transition: none !important; scroll-behavior: auto !important; } } No speech media or sound playback: captions and sound equivalents are currently N/A. Progress is visible as text and a pulse. No live text sits over raster images, so the 4.5:1 text-over-image test is N/A. Source: supplied part_b.md, B3. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 11
PART C / MULTIMEDIA PRESENTATION
MY AITU / ICT ASSIGNMENT 4
11 / 19
Show the product.
Tell its story.
A narrated walkthrough of the My AITU / LMS bridge.
2:10
planned running time
01
Sign in
02
Explore
03
Explain
04
Look ahead
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 11 Part C — Multimedia presentation Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 12
C1 / STORYBOARD
A clear role for every narrator.
Four scenes connect the working prototype to its purpose and next steps.
MY AITU / ICT ASSIGNMENT 4
12 / 19
TIME | ON SCREEN | NARRATOR | TALKING POINT
0:00–0:30 | Login screen | Nurassyl | Explain how sign-in works.
0:30–1:10 | Main pages and navigation | Salima | Walk through content and design decisions.
1:10–1:40 | Statistics and Stage 1 survey | Azhar | Explain the project’s purpose.
1:40–2:10 | Demo sketches | Azhar | Outline the project’s future.
TOTAL · 2 MIN 10 SEC
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 12 C1. Storyboard Duration What is on screen Narration 0:00-0:30 Login screen Nurassyl: How login proccess looks 0:30-1:10 Main pages, burger-menu, references from stage 1 Salima: Website content and design desecions 1:10-1:40 Statistics, survey from stage 1 Azhar: the purpose of project 1:40-2:10 Demo sketches Azhar: Future of the project Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 13
C2 / THE VIDEO
Open the project demonstration.
MY AITU / ICT ASSIGNMENT 4
13 / 19
My AITU / LMS bridge
Team walkthrough · Google Drive folder
OPEN VIDEO FOLDER
Scan to open
Opens the project’s
Google Drive folder.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 13 C2. The video https://drive.google.com/drive/folders/1izH4jyb1Ooi-pvghCGhOfCXmk6A6rqKn?usp=sharing Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 14
C3 / PRODUCTION NOTE
The plan is defined. Export details remain.
MY AITU / ICT ASSIGNMENT 4
14 / 19
Production note
The storyboard plans a 2-minute 10-second walkthrough of the My AITU / LMS bridge, with narration from all three team members. It covers sign-in, key pages, the project’s purpose and future work. MP4 with H.264 video and AAC audio is the planned delivery format for broad device playback. The linked Drive folder is the hand-off location. Recording and editing tools, final resolution, frame rate, bitrate and file size were not supplied, so they cannot yet be reported as completed production settings. These values should be checked against the final exported video before submission.
FINAL FILE NOT INSPECTED
Confirm before
submission
Recording + editing tools
Resolution + frame rate
Video + audio bitrate
Final duration + file size
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 14 C3. Production note In 80–120 words, state the tools you used to record and edit, and your export settings — container, codec, resolution, frame rate, bitrate and final file size — and explain why you chose them rather than a higher or lower setting. Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 15
PART D / INTEGRATION
MY AITU / ICT ASSIGNMENT 4
15 / 19
From media assets
to a working bridge.
The multimedia layer supports the same project and prototype.
01
Sign in
Individual user session
→
02
Read LMS
Course and attendance data
→
03
Present clearly
A responsive student interface
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 15 Part D — Integration with the project Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 16
D1 / UPDATED PROTOTYPE
Run the project from its repository.
Linux launch sequence from bridge-test/README.md.
MY AITU / ICT ASSIGNMENT 4
16 / 19
01
Clone the project
git clone https://github.com/d30mantcoder/ICTProject
02
Create an environment
cd ICTProject && python -m venv venv
03
Install dependencies and Chromium
venv/bin/python -m pip install -r bridge-test/requirements.txt
venv/bin/python -m playwright install chromium --only-shell
04
Launch the bridge
BRIDGE_HEADLESS=1 venv/bin/python bridge-test/app.py
OPEN REPOSITORY
Local address
127.0.0.1:1740
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 16 https://github.com/d30mantcoder/ICTProject Git clone it Create virtual environment Install dependencies (requirements.txt) Run bridge-test/app.py via python D1. Updated prototype Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 17
D2 / CHANGE LOG
Three changes that make the bridge useful.
MY AITU / ICT ASSIGNMENT 4
17 / 19
CHANGE | WHY IT WAS NEEDED | CURRENT BEHAVIOUR
Real LMS data | A prototype needs useful, current course information. | Reads the user’s LMS content.
Interface redesign | Frequently used tasks were hard to reach. | Key actions are brought to the main page.
Asynchronous sessions | The earlier flow could not support independent users. | Users have separate sessions; slow requests do not hold others.
SCALE LIMIT STILL OPEN
<3 seconds per request at 1,000 users has not been verified.
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 17 D2. Change log Change Reason Status Added fetching from LMS To make the website usable Using real LMS data Redesign of UX of LMS UX of original LMS was uncomfortable Most useful buttons takes place on the main page Added asynchronius sessions It was impossible to work for more than 1 person at the same time before Server handles multi-user sessions Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 18
D3 / TEAM CONTRIBUTIONS
One project. Three areas of ownership.
MY AITU / ICT ASSIGNMENT 4
18 / 19
SZ
Salima
Zimbekkyzy
PARTS C + D
Video editing
AS
Azhar
Saparzholova
PARTS A + D
Multimedia format comparison
NO
Nurassyl
Oralbekov
PARTS B + D
Media integration and optimisation
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 18 Members Parts Contribution Salima C,D Editing the video Azhar A,D Nurasyl B,D contribution table D3. Comparing the multimedia formats Integration and optimization of multimedia Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.

## Slide 19
THANK YOU
MY AITU / ICT ASSIGNMENT 4
19 / 19
Less weight.
More clarity.
Multimedia choices that support a better student experience.
73%
smaller preview
18
inline SVG icons
25
inventoried assets
Notes: SOURCE CONTENT FROM ORIGINAL SLIDE 19 Thank You Design revision: explicit text areas, stable fonts and editable tables. JPEG measurements added from supplied screenshot.